## Slide 1: Review of the MiSTer Gamming Console
Jim Brakefield
IEEE San Antonio Computer chapter
19 Feb. 2020
https://events.vtools.ieee.org/m/220917

## Slide 2: IO card, FPGA card & USB hub
RAM card tucked next to IO card
http://emulation.gametechwiki.com/index.php/MiSTer
https://github.com/MiSTer-devel/Main_MiSTer/wiki

## Slide 3: MIST project https://github.com/mist-devel/mist-board/wiki

## Slide 4: MiSTer FPGA card https://www.terasic.com.tw/cgi-bin/page/archive.pl?Language=English&CategoryNo=167&No=1046

## Slide 5: Similar FPGA cards

## Slide 6: Raffle FPGA card (DE10-Standard)
http://modernhackers.com/porting-mister-to-arrow-sockit-fpga/

## Slide 7: MiSTer mantra: exact replica
MiSTer is an open project that aims to recreate various classic computers, game consoles and arcade machines, using modern hardware. It allows software and game images to run as they would on original hardware, using peripherals such as mice, keyboards, joysticks and other game controllers.

## Slide 8: Open Source
Bare add-on cards with CAD files
  IO card: RGB, Audio, Fan
  Memory card: 128MB SDR RAM: https://misterfpga.co.uk/ required by some games (recommended)
  USB port expander
FPGA projects (142 of them)
  Altera/Intel Quartus (lite/free version)
  Complete Quartus projects: *.qpf files
  Use open source microprocessor cores (Z80, 6502, …)

## Slide 9: Alternatives
Gaming console & cartridge
  Legacy: Nintendo, etc.
  Modern: Playstation, etc.
PC with fast graphics
Open source game software:
https://en.wikipedia.org/wiki/List_of_open-source_video_games
  PC
  Raspberry Pi

## Slide 10: Available MiSTer “games”
Consoles: http://emulation.gametechwiki.com/index.php/MiSTer
Arcade games: https://github.com/MiSTer-devel/Main_MiSTer/wiki/Arcade-Cores-List
DIY: Register & download Quartus Lite
  Select the most similar project & modify

## Slide 11: MiSTer FPGA card
Cyclone V FPGA chip with:
  Two ARM Cortex A9 at 800 MHz
  110K “logic cells”
  502KB of block RAM (e.g. > 64KB of 8-bit uP)
  112 hardware multipliers
Two pair of 20-pin IO
Arduino IOs
1GB DDR3
HDMI video out
Linear Technology A2D & D2A add-on card

## Slide 12: DE10-nano SD card
Runs on FPGA ARM Cortex A9 core
Linux environment
FPGA fabric independent from ARM cores
Works with Quartus

## Slide 13: Intel/Altera Quartus https://www.intel.com/content/www/us/en/software/programmable/quartus-prime/overview.html
Software for utilizing Intel/Altera FPGAs
Supports: Verilog, VHDL & System-Verilog RTL (Register Transfer Languages)
Editor, compiler, place & route and bit file generation
Free IP (Intellectual Property) such as memory, DSP, FFT, serial ports, etc. (see also https://opencores.org/)
Have training videos, trade shows & seminars

## Slide 14: MiSTer SD card
https://github.com/MiSTer-devel/Main_MiSTer/wiki/Folders-and-File-naming
Linux environment
Root directory holds FPGA .rbf files
Other directories hold game cartridge ROM files
Keyboard F12 used to escape current game
Update script refreshes all games/consoles/uP

## Slide 15: MiSTer impressions
Well documented
Well organized and consistent
Many YouTube videos
SmokeMonster commentary on arcade cores
  Has list of games running on bare FPGA board

## Slide 16: SDRAM requirements
https://github.com/MiSTer-devel/Main_MiSTer/wiki/SDRAM-Requirement-by-cores
https://www.retrorgb.com/mister-cores-without-add-on-boards.html