## Slide 1: Small Chip Landscape Jim Brakefield jim.brakefield@ieee.org
The smallest parts commercially available

## Slide 2: Reasons for Small
Lower power
  Battery driven design
  Thermal management is simpler
Lower cost: silicon area savings are passed on
Newer/smaller chips are faster and more capable
Use single PCB
  Connectors are a weak point
Lower weight
And of course, less volume: in X, Y and Z

## Slide 3: IC Transistor Density
7nm process: ~100M transistors / mm2
  https://en.wikipedia.org/wiki/7_nm_process
Small uP: 10K transistors
  https://en.wikipedia.org/wiki/Transistor_count
  RISC uP with cache: 1M transistors
  Large FPGA: 100 billion transistors
  Single chip stacked flash: 2 trillion transistors
    Multiple chips in single package

## Slide 4: PCB fabrication
Use CAD package to input schematic
  Auto or manually route signal traces
Generate Gerber files
Have PCB fabricated
Send chips and PCBs to assembly house
  Or DIY with hot air gun or oven
See if board works
Solder stencils now optional: can ink-jet print solder paste

## Slide 5: LCD Digital Microscope
Battery powered
HD resolution
LED illumination
Many products all
made by the same
company

## Slide 6: Digital Tweezers
Miniware DT71 Mini Digital Tweezers
Resistance, Capacitance, Inductance, Voltage & Frequency

## Slide 7: Small Packages

## Slide 8: Digital logic
nexperia two input XOR gate 74LV1T86GXH
  0.8mm by 0.8mm by 0.35mm = .64mm2 and .224mm3
  Five pin QFN package
  0.8 to 3.3 vdc
  100X area advantage
Compare with TTL logic
  11mm by 20mm by 8 mm
  16 pins
  5.0 vdc
  Uses both sides of PCB

## Slide 9: Small FPGA chip
Latticesemi ICE40UL1K
  1.4mm X 1.4mm X 0.6mm = 1.99mm2 & 1.19mm3
  10 user IOs
  Flash, I2C, SPI, PWM & oscillator built-in
  1.2 vdc to 3.3 vdc IOs
  1280 LUTs, 14 block RAMs

## Slide 10: Small uP chip
Atmel/Microchip AVR ATTINY20
1.4mm by 1.56 mm WLCSP package
2K bytes of flash
10-bit A2D
IO: PWM, I2C, SPI, …
Same uP as Arduino

## Slide 11: 3D gyro& 3D accelerometer combo
Invensense MPU-9250
  3mm X 3mm X 1mm
  24 pins, I2C and SPI
  Three stacked chips
  Includes signal processor
  Add pressure sensor for complete inertial package
    Bosch BMP183: 3.6mm x 3.8mm
    1 foot altitude resolution

## Slide 12: Silicon oscillators
SiTime SiT1532
  0.8mm X 1.5mm X 0.55mm = 1.2mm2 & 0.66mm3
  4 pins, 32.768KHz
  Frequencies to 200MHz in standard oscillator packages
  Very low jitter

## Slide 13: LED
Rohm SLMP34 RGB LED
  1mm X 1mm X 0.2mm = 1mm2 and 0.2mm3
  4 pins, VF RGB of 2.2, 3.3 & 3.2vdc
Rohm SLM-P1
  1mm X 0.6mm
  Single color

## Slide 14: Resistors, capacitors & inductors
Standardized sizes in hundredths of inch (mm)
  01005 (0.4 x 0.2 x .13), 1/32 watt, “black dots”
  0201 (0.6 x 0.3 x .23), 0.05 watt
  0402 (1.0 x 0.5 x .35), 0.1 watt
  0603 (1.6 x 0.8 x .45), 0.1 watt, sometimes printed number code
  0805 (2.0 x 1.25x.60), 0.125 watt
  1206 (3.2 x 1.6 x .60), .25 watt
  2010 (5.0 x 2.5 x .60), .5 watt
  2512 (6.4 x 3.2 x .60), 1 watt
Color: 01005 0201 0402 0603 0805 1206
  resistors: black
  caps: light brown
  inductors: ferrite
1210, 1812, 2010, 2512 =>

## Slide 15: Digital cameras
OmniVision OV6948(200x200 pixels)
  0.75mm X 0.75mm, thickness depends on lens
  4 pins
  Fixed focus
Digital Optics mems/cam
  8mm X 8mm X 5mm
  Autofocus
  UWXGA

## Slide 16: Radio
Nordic Semi: Nrf52805 low power Bluetooth
  2.5mm by 2.5mm by 0.5mm
  Includes ARM cortex M4 uP
Taiyo-Yuden AF216M245001 antenna
  2.5mm by 1.6mm by 1.6mm = 4mm2 and 6.4mm3
  2.4GHz band

## Slide 17: Places to get chips
www.digikey.com original mail-order house
www.mouser.com some parts only at mouser
www.newark.com stock scopes & such
www.avnet.com high volumes
www.arrow.com high volumes
Manufacturer’s web sites
Keep an eye on inventory levels:
  choose popular and stocked parts if possible

## Slide 18: Some chip Manufacturers
actel (now microsemi), altera, amd, analog (devices), arm, atmel, austriamicrosystems, bosch, cirrus, cree, cypress, diodes, everspin, fairchildsemi, freescale, ftdichip, hittite, holtic, ibm, idt, infineon, intel, intersil, issi, latticesemi, linear, marvell, maxim-ic, microchip, micron, national (now TI), nec, nordic, nvidia, nxp, okisemi, onsemi, panasonic, rabbitsemiconductor, renesas, samsung, silabs, spansion, sst, st, ti, toshiba, we-online, xilinx, xmos, zilog
FPGA uP analog memory diverse passives simple

## Slide 19: Keeping Up-to-date
Trade shows
  Embedded Systems Conference
Magazines: requires business address & web site
  EE Times
  Electronic Products
  EDN (Electronic Design News)
  Many others: PCB design, Specialty markets
News Letters
  Manufacturers
  Trade Press (weekly)
  Distributors
  Tool vendors

## Slide 20: Tiny 32-bit Microprocessor
Freescale Kinetis KL02 ARM Cortex M0
  1.9mm X 2.0mm X 0.4mm = 3.8mm2 and 1.5mm3
  18 user IOs, 32KB flash, 4KB ram, 48MHz
  UART, SPI, (2) I2C, (2) PWM, 12-bit ATD

## Slide 21: ARM chips
www.keil.com/dd/chips/all/arm.htm
  Massive list of the more than 1200 distinct ARM chips that are supported by Keil
  A summary sheet for each part
At Digikey or Mouser or Newark:
  Search on “microcontrollers” or “microprocessors”
  Narrow to an ARM family
  Manufacturer sites
  Comparison spreadsheets for each uP family

## Slide 22: 9D inertial sensor breakout boards

## Slide 23: Package comparisons