## Slide 1: FPGA Timeline & Applications FPGAs past, present & future
Jim Brakefield

## Slide 2: FPGA Application Areas
Communications
DSP
Software-defined radio
Aerospace and defense systems
ASIC prototyping
Medical imaging
Computer vision
Speech recognition
Cryptography
Bioinformatics
Computer hardware emulation
Data Center: AI, NN, big data
$6-7B yearly sales
Advantages:
Low NRE
Low volume products
Updates/patches
Parallelism
Portable code (RTL)
Soft dev || Hard dev
Early use of process nodes
Disadvantages:
ASICs are cheaper,
faster and lower power
in high volumes

## Slide 3: Low End Applications
Glue logic Connection of disparate devices to a uP
Last minute patches
Logic funnel Legacy design re-hosting
IP: pre-packaged modules
Soft core processors & peripherals (www.opencores.org)
1.5-3mm pkg, 2K LUTs
.1Mb block RAM
20K LUTs, 40 DSPs,
1Mb block RAM

## Slide 4: Mid-scale Applications
Communications: Internet routers, Telephone switches, Protocol conversion
Signal Processing: Software defined radio, Camera, Audio, Video, Radar …
Test & Measurement: high speed A2D & D2A,
Big science: Super-collider, SETI, etc.
Aerospace: radiation hardened, military temperature range
SOC (System On a Chip): driverless vehicles
200K LUTs, 1K DSPs,
15Mb block RAM

## Slide 5: High End Applications
ASIC (Applications Specific Integrated Circuit) emulation
High end weapons, who knows what else?
Super-computing coprocessor
Intel bought Altera
Wall street (high frequency trading)
AI/deep NN/data center acceleration
2.5M LUTs, 5K DSPs,
200Mb block RAM

## Slide 6: The Vendors
Xilinx: www.xilinx.com
  Originated FPGAs, tried anti-fuse, flash & CPLD, now #1
Altera (now Intel): www.altera.com
  Originally CPLDs, currently #2 in FPGAs.
Microsemi (was Actel): www.actel.com
  Originally anti-fuse, then flash, now SRAM & flash based
Lattice Semiconductor: www.latticesemi.com
  Offer tiny FPGA chips, diversifying away from FPGAs
uP with some programmable logic
  Cypress (under PSoC): ARM + programmable IO
  Atmel/Microchip: ibid.

## Slide 7: The FPGA
Generic FPGA diagram
Green: IOs
Squares: LUT
groups/slices/blocks
Octagons: Wiring
interconnections
Lines: Wire
segment bundles
From: Trimberger, 2015 Proc IEEE v103 #03 pg320

## Slide 8: FPGA timeline
From: Trimberger, 2015 Proc IEEE v103 #03 pg318
Not far off:
1GHz performance
7nm silicon
On chip DRAM

## Slide 9: Basic LUT (Look-Up Table)
1985 LUTs plus DFF Xilinx XC2000
  Clocking facilities
  Configuration memory
  Routing wires
1991 Carry chain Xilinx XC4000
  LUT RAM (16x1)
  Shift Registers
Currently up to 2.5M LUTs
at 100-1000 LUTs/$

## Slide 10: LUT + DFF
Lattice Semiconductor iCE40FamilyHandbook.pdf pg6-2
3LUTs tried
6LUTs in use
ALM: ~two
5LUTs
with
multiple
configurations
4LUT: 16 bits
of memory &
a 16:1 MUX

## Slide 11: Uses:
“glue” logic
Reprogrammable (field changes)
Reliability
(parts count and wiring reduction)
IPo1553 module (BAE Systems): ARINC 429, MIL-STD 1553, RJ45, CAN

## Slide 12: Block RAM
1995 Dual port RAM Altera FLEX
Variable aspect ratio (on each port)
  16Kx1, 8Kx2, 4Kx4, 2Kx8/9, 1Kx16/18, 512x32/36
A variety of RAM capacities
  LUT RAM (16x1), small block RAM (~32x18), block RAM (~512x36), large block RAM (~4Kx72)
Uses:
  Buffers, FIFOs, shift registers, scratch pad memory, DSP coefficients, two single port RAMs, u-code
up to ~12K block RAMs
up to 480M bits

## Slide 13: Block RAM
Data in
Parity data in
Address in
Write enable
Enable
Reset
Clock
Xilinx Spartan-6 FPGA Block RAM Resources User Guide pg12
Data in
Parity data in
Address in
Write enable
Enable
Reset
Clock
Data out
Parity data out
Data out
Parity data out
Parity bits
usable as
data bits

## Slide 14: PLL (Phase Locked Loop)
1996 Altera FLEX 10K
FPGAs can have dozens of distinct clocks
All the analog (of the PLL) inside FPGA
Uses: Reduce chip count, precise clock phase control
FPGA internal clocks to 800MHz

## Slide 15: “ASIC” IO
1998 Universal IO Xilinx Virtex
1.2, 1.8, 2.5, 3.3, 5.0 VDC
  each bank of IO pins has its own power supply
LVTTL, CMOS, HSTL, SSTL, PECL, LVDM …
  (via constraint file)
4, 8, 12, 16, 24ma, pullup/pulldown (ibid)
resistive termination, slow/fast edges (ibid)
Uses:
  general purpose IO, DRAM hookup, PWM, logic analyzer, etc.

## Slide 16: “ASIC” IO
Lattice Semiconductor iCE40FamilyHandbook.pdf pg6-7
Global input buffers used for clocks and reset
To Device Pin
Up to 1680 IOs/chip

## Slide 17: Multiply/accumulator
2000 18x18 signed Xilinx Virtex-2
2002 DSP block Altera Stratix
Initially no accumulator, accumulators now include ALU capability and floating-point
Use pipelining for maximum speed
Multiplier shapes: 16x16, 18x18, 18x27; (3)9x9, (2)18x18 or (1)27x27
Uses: DSP, FFT, ALU
up to ~12K per chip
running at 800MHz

## Slide 18: Simplified DSP slice
Xilinx Spartan-6 FPGA DSP48A1 Slice pg 17

## Slide 19: SERDES (Serialize/De-serialize)
2001 Source synchronous transceiver Xilinx Virtex-II
2002 SERDES Transceiver
Xilinx Virtex-II Pro
Uses:
  Communication links: Fiber connections, Ethernet, PCI-express, Interlaken, etc
up to ~100 per chip
up to 56Gbps

## Slide 20: ASIC micro-processor(s)
2000 ARM 9 Altera Excalibur
2002 PowerPC Xilinx Virtex-II Pro
2010 ARM Cortex M3 Actel Smart Fusion
2010 ARM dual Cortex A9
Xilinx Zynq, Altera Cyclone V
2015 ARM quad A53 & dual R5, GPU
Xilinx Zynq Ultrascale+, Altera Arria-10
2019 ACAP Xilinx datacenter compute chip
2019 ? Intel/Altera ?
All have microprocessor peripherals
Uses: Reduce chip count, cleaner interface between uP and FPGA fabric
1 to 6 per chip, 100MHz to 1.5GHz

## Slide 21: SOC chip
From: Trimberger, 2015 Proc IEEE v103 #03 pg327

## Slide 22: Zynq: ARM + FPGA chip
HC23.18.322.Zynq-7000-EPP-Dutta_Xilinxrevised.pdf

## Slide 23: Silicon interposer (3D silicon)
2009 Multi-chip FPGA Xilinx Virtex-6
Uses: Yield improvement, reduced wiring capacitance, augmentation with SERDES, DRAM & A2D/D2A chips
Thousands of wiring channels
Xilinx white paper #380 pg 4 & 7, 2012: Stacked Silicon Interconnect Technology

## Slide 24: HLS (High Level Synthesis)
1980s VHDL & Verilog RTL
  (Register Transfer Language)
2004 C, C++ or SystemC to VHDL/Verilog
Matlab to VHDL/Verilog
2011 Xilinx bought AutoESL, incorporated HLS technology into their Vivado tool.
2011 OpenCL for uP, DSP, GPU & FPGAs
Uses: Productivity
FPGA development by software engineers
“Work in Progress”

## Slide 25: Floating-point
2015 32-bit Add/subtract/multiply Altera Arria-10 & Stratix-10
IEEE floating-point library: exponent & mantissa size bit adjustable
Uses:
  Super computer applications
  Wide dynamic range DSP

## Slide 26: 2019 High End Processing
High performance PC: x86, 64-bit ARM, etc
DSP: the niche is evaporating/morphing
ASICs: high NRE
GPGPU (General Purpose Graphics Proc. Unit)
  Originally for gaming, now used for AI apps
FPGAs (Field Programmable Gate Arrays)
  As chip capacity increases, capabilities escalate

## Slide 27: 2019 Xilinx ACAP: Adaptive Compute Acceleration Platform
  https://www.eejournal.com/article/xilinx-previews-next-generation/
HW/SW programmable engines
  Probably enhanced DSP modules
  https://www.youtube.com/watch?v=XMeKwtI82M8
Application and Real-Time Processors
  Probably ARM or RISC-V uP
On-die network fabric
  See Jan Gray’s http://fpga.org/grvi-phalanx/

## Slide 28: 2019 Intel/Altera:
Singularity Prosperity series of videos:
  https://singularityprosperity.com/videos
  The Future of Classical Computing (Heterogeneous Architecture – CPUs, GPUs, FPGAs, ASICs,...):
  https://www.youtube.com/watch=2yklU69Xiuo
  The GPGPU (nVidia) argument:
  https://www.youtube.com/watch?v=658n_Ym8dkk
Intel has many irons in the fire, along with Microsoft, Google, …
  https://www.nextplatform.com/2018/05/24/a-peek-inside-that-intel-xeon-fpga-hybrid-chip/

## Slide 29: References
Three Ages of FPGAs: A Retrospective…, Steve Trimberger, Proc. IEEEE v103#3p318, 2015
  www.cpe.virginia.edu/grads/pdfs/January%202016/VLSI.pdf
  forums.xilinx.com/t5/Xcell-Daily-Blog/Video-The-Three-Ages-of-the-FPGA-and-the-Age-of-the-Design/ba-p/644396
Xilinx Part Family History, John Lazzaro,
  www-inst.eecs.berkeley.edu/~cs294-59/fa10/resources/Xilinx-history/Xilinx-history.html
Altera History, corporate,
  www.altera.com/about/company/history.html
HLS (High Level Synthesis)
  en.wikipedia.org/wiki/High-level_synthesis

## Slide 30: High End Applications
Typical FPGA & uP module

## Slide 31: High End Applications
ALDEC HES-7
Board using
(6) Virtex-7 2000
with 1.1M LUTs
each
Used to simulate
600M ASIC gates

## Slide 32: Actel SmartFusion2 KickStart Kit
Avnet
AES-SF2-KSB-G
$59.95
Has ARM
Cortex M3

## Slide 33: Xilinx Zynq SOC kit
Snickerdoodle with WiFi & Bluetooth $72

## Slide 34: Altera Cyclone V SOC kit
Terasic
DE-0
Nano SoC
$99

## Slide 35: Cypress PSoC5 kit
CY8CKIT-059 for $10 with: ARM Cortex M3, Analog & Digital IO

## Slide 36: IP (Intellectual Property) Pre-packaged modules, macros & generators
TTL logic equivalents (with schematic entry)
Simple macros (also with schematic entry)
Vendor free IP: soft-core processors, CORDIC, FFT, Floating-point, PCI-express, memory controllers …
Open source IP: www.opencores.org
Vendor and 3rd party non-free IP (various interfaces, soft core processors, image processing…)
Uses: save time & money

## Slide 37: Xilinx CORDIC GUI
Ray Andraka 1998: A survey of CORDIC
algorithms for FPGA
based computers

## Slide 38: Intro: Experience
PowerPC emulation of Pentium
  Decided to learn VHDL 1995
AMD/Vantis/Lattice Semi
  Competitive benchmarking 1998-2002
OnBoard Software/BAE Systems 2004-2012
  FLR-9, IP over 1553, Weather RADAR
ROIS24_24uP
  24-bit soft core processor 2016

## Slide 39: FPGA Code & Test Process
Schematic capture (doesn’t scale)
Or write RTL (Register Transfer Logic) which evolved into Verilog and VHDL (1980s)
Simulate
  Faster than compile/map-pack-P&R-bit-stream/download
  Use test-bench
  Not perfect
Compile: synthesize VHDL/Verilog to gates or FPGA primitives
Map, Pack, timing driven Place & Route
Bit-stream generation
Download & test