## Slide 1: Provisioning a 64-bit processor (with 264 bytes of memory)
Jim Brakefield

## Slide 2: Purpose of the talk
To give a sense of where we are
To give a sense of scale
To give a sense of history
To show where the limitations are
  Simple way to understand the computer industry
Design regime is “lowest cost”
  Simplifies design choices

## Slide 3: The Grains of Rice (Bytes) on a Chessboard
1st row has 255B tiny piece of silicon
2nd row has 65KB minor piece of silicon
3rd row has 16MB fraction of a memory chip
4th row has 4GB fraction of a flash drive
5th row has 1TB fraction of a disk drive
6th row has 256TB 24 large (12TB) disk drives
7th row has 64PB ~6400 large disk drives
8th row has 16EB ~2M large disk drives

## Slide 4: Powers of two
210 =1.024* 103 Kilo(byte) thousand
220 =1.049* 106 Mega million
230 =1.074* 109 Giga billion
240 =1.099* 1012 Tera trillion
250 =1.125* 1015 Peta quadrillion
260 =1.153* 1018 Exa quintillion

## Slide 5: A review and an extrapolation
Will be addressing memory capacity
When RAM gets too expensive, use virtual memory
28 = 256 byte computing
216 = 64KB computing
232 = 4GB computing
  12 bytes for each person in US
248 = 256TB computing
  32K bytes for each person in world
264 = 16EB computing
  Really, really huge

## Slide 6: Technology Eras (design)
Electro-mechanical
  Desk calculators, tabulating machines, printers
Vaccum tube
  1940s thru mid 50s (giant brains)
Transistor
  Late 50s thru mid 60s (corporate level adoption)
TTL
  Mid 60s thru 70s (department level adoption)
IC
  Early 70s thru today (personal computer & cellphone)

## Slide 7: 8-bit addressing
256 bytes, 64 words
First example: Zuse T-3 in 1941
  Relays, film strip used for program
Today’s chips
  As low as 10 cents each in volume
  Low pin counts
  Limited RAM (<256 bytes) and limited program
  Self contained
  Used in simple controller applications

## Slide 8: “8-bit” computers
Zuse Z3 replica Deutsches Museum, Munich
Small processor chips from Padauk

## Slide 9: 16-bit Addressing
64K bytes
First example: Whirlwind in 1951
  Vacuum tube logic
  Initially Williams tube, converted to core
  Essentially a “mini-computer”
  Technology prototype for SAGE computer

## Slide 10: 16-bit computers
Whirlwind at Museum of Science, Boston
Core memory stack inside open rack
Texas Instruments
eZ430-Chronos-915
development kit

## Slide 11: 16-bit Addressing cont’d
Today’s chips
  As low as $1 each in volume
  Modest pin counts
  Modest RAM and limited program
  Self contained
  Usually programmed in high level language
  Whole raft of peripherals
  Is under pressure from 32-bit processors

## Slide 12: 32-bit Addressing
4 Gigabyte address space
  Motivation for virtual memory
  Pioneered by IBM 360 in 1964
  Virtual memory added in 1967 for Un. Michigan
  Initially had a 24-bit address (16 megabytes)
  Disk drives for gigabyte storage

## Slide 13: 32-bit Addressing cont’d
Today represented by Raspberry Pi Zero
  $10 includes chip, IO, memory and gigabyte flash
  Linux operating system
  20 million Raspberry Pi sold so far
Cell phones contain same microprocessor
  Billions sold
Individual 32-bit chips for under $1
  Sans virtual memory

## Slide 14: 32-bit computers
IBM360-67 at Michigan Terminal System
Raspberry Pi Zero

## Slide 15: Historical Omissions
36-bit computers
  IBM 700 series, Univac 1100 series, GE 600 series
  Was the era of 6-bit characters, no lower case
  https://en.wikipedia.org/wiki/36-bit
Early (limited) virtual memory
  both 48-bit word size machines, 1961 & 1962
  Burroughs B5000 & Manchester Atlas-1
History of the PC
  Originally 16 bit, then 32 bit and now 64 bit

## Slide 16: Historical Omissions cont’d
Real Machines with 24-bit and 48-bit words
  http://www.quadibloc.com/comp/cp0303.htm
Real Machines with 16, 32, and 30-bit words
  http://www.quadibloc.com/comp/cp0304.htm
Still More Real Machines (12-bit words)
  http://www.quadibloc.com/comp/cp0305.htm
History of Digital Equipment (DEC)
  12, 16, 18, 32, 36 & 64-bit: Transistor, TTL & IC

## Slide 17: 48-bit Addressing
Today’s high end 64-bit processors limit virtual addressing to 48-bits = 256 Terabytes
  Mostly no need for a larger address space
  Clock rates above 2 GHz
  Multiple cores with four & eight cores common
  Used in cell phones, tablets, PCs, internet servers and supercomputers
  Power consumption ranges from 1 to 100+ watts

## Slide 18: 48-bit Provisioning (on the cheap)
Single board computers
  Raspberry Pi 3B+ $35 57 by 86 mm
    No SATA, no M.2, 40 pin IO header
  Banana Pi W2 $93 105 by 148mm
    (2) SATA, 1Gbps Ethernet, (3) M.2,
    10 watts, 2GB RAM, 40 pin IO header
  UDOO BOLT $300 120 x 120mm
    (2) SATA, 1Gbps Ethernet, (3) M.2,
    50 watts, up to 32GB RAM, 40 pin Arduino header

## Slide 19: 48-bit Provisioning cont’d
So, need the following:
16 Banana Pi or Udoo Bolt $2-5K
32 High capacity disk drives $8K
As much M.2 flash drive as one can afford
16 port Ethernet switch
Total $10-20K
Within the range of an expensive hobby or grant money or engineering project

## Slide 20: 48-bit Provisioning cont’d
Use cases:
  Video server
  Keeping track of everything
  Real time video processing (self driving cars)
  Big data
  Deep neural nets
Intel M.2 SSD
card with 2TB
1.8GBps read
Speed
22x80mm

## Slide 21: 48-bit computers
45drives.com Storinator file server
Back of chassis has large dual
socket x86 board with disk drive
connections and high speed
Ethernet connections
12TB Seagate 3.5” disk drive

## Slide 22: 56-bit Provisioning
Disk drives $37 per TB
  “Enterprise class” disks for best MTBF
  Housed in large chassis
Disk drives separated from computers
  High speed network connections
  Dedicated file servers
Want/need redundancy
  Both in disk contents and location
  Redundant power supplies & utility feeds

## Slide 23: 56-bit Provisioning cont’d
An active market for corporate data sets
Super computers focus on compute power
No low budget solutions
Use cases
  Internet archive 30PB (currently)
  Facebook 100PB (in 2012)
  Texas Advanced Computing Center
    https://www.tacc.utexas.edu/about/timeline

## Slide 24: 56-bit computer
Data Direct Networks (DDN)
SFA14K file server
(rack of ~1000 disk drives)
Repeat six times for 64PB
8x InfiniBand and 40/100GbE
Ethernet connections
DDN mentioned in
University of Texas “Frontera”
Supercomputer press release

## Slide 25: The 64-bit Super-Computer
IBM 7030 Stretch was first attempt 1961
  64-bit word size, 24-bit address
CDC 6600 in 1964 was three times faster
  10 MHz clock, multiple arithmetic units
  Stretch could not compete on price
Cray-1 followed in 1974
  80 MHz clock, pipelined arithmetic units
Single chip DEC Alpha in 1992
  Initially 150 MHz, eventually 1.3 GHz clock

## Slide 26: Some Constraints
RAM 128GB SIMMs $5K/TB
SSD 4TB M.2 Card $150/TB
Disk 10TB consumer grade $30/TB
Disk 12TB enterprise grade $37/TB
Disk tray holding 45 disks $6K+
Single board computer: ARM $100
Single board computer: x86-64 $300+
Server grade x86-64 “blade” $2K+

## Slide 27: 64-bit Provisioning
This is 256 times the size of the 56-bit system!
The cost is affordable to:
  Multi-Billionaire?
  Large internet company
  Governments
Use case is?
  Mirror the internet
  Model the human brain

## Slide 28: 64-bit Provisioning cont’d
Some new wrinkles:
Reliability
  A disk drive failing every hour
  A processor card failing every hour
Power consumption in the many megawatts
Software challenges

## Slide 29: The Grains of Rice (Bytes) on a Chessboard
1st row has 255Bytes $0.10 chip
2nd row has 65KiloB under $1 chip
3rd row has 16MegaB CPU & memory chip
4th row has 4GigaB Raspberry Pi, SD card
5th row has 1TeraB SBC & disk drive or PC
6th row has 256TeraB Electronics chassis
7th row has 64PetaB 6 Racks for file server
8th row has 16ExaB Large room for file server

## Slide 30: In Summary
8-bit computers are everywhere
16-bit computers are everywhere
32-bit computers are cheap
64-bit computers in high end cellphones
48-bit (256 terabyte) virtual memory possible but not cheap
64-bit (16 exabyte) virtual memory challenging and definitely not cheap

## Slide 31: 8, 16 & 32-bit processors for under $1
A review of 21 different processor chips
  https://jaycarlson.net/microcontrollers/
This is for the embedded market where cost is paramount.
Program memory is usually on-chip flash
Each chip family is available in hundreds or thousands of variations in memory size, IO devices, speed and performance.

## Slide 32: 64-bit Provisioning cont’d
Interconnection challenges
  Most supercomputers use a 3D torus interconnect
  Most CPU interconnects are proprietary
  CCIX: cache coherent shared virtual memory
    https://www.ccixconsortium.com/

## Slide 33: Outline
Structure of the talk
  Part history, part current technology
  Simple way to understand the computer industry
Review of powers of two
The sequence
  8-bit, 16-bit, 32-bit, 48-bit & 64-bit addressing